## Slide 1
DLT Camera Calibration
Varga Andrei Radu, 30433
Image Processing

## Slide 2
Dataset
OpenCV Checkerboard Images (left01.jpg – left14.jpg)
Included with OpenCV in samples/data/
https://github.com/opencv/opencv/tree/4.x/samples/data https://www.kaggle.com/datasets/kalpitnathan/multi-camera-calibration-test-dataset https://huggingface.co/datasets/bigbitbus/chess
7×6 inner corners per image
14 images from different viewpoints
~42 point correspondences per image
3D world coordinates: known regular grid on Z=0 plane

## Slide 3
Libraries
C++ — OpenCV only for image I/O and corner detection python
OpenCV (image handling only)
cv::imread, cv::findChessboardCorners, cv::cornerSubPix, cv::drawChessboardCorners.
Eigen
Matrix and vector operations (Eigen::MatrixXd, Eigen::VectorXd). SVD computation via Eigen::JacobiSVD for solving the homogeneous system Mv = 0. General linear algebra (transpose, inverse, norms).
Implemented by me:
DLT system matrix construction, coordinate normalization, RQ decomposition (Gram-Schmidt / Givens rotations on the 3×3 submatrix of P), reprojection error computation. All implemented from scratch following the lecture.

## Slide 4
DLT Pipeline
1. Detect checkerboard corners -- 2D image points
2. Define 3D world points (known grid, Z=0)
3. Normalize 2D and 3D coordinates
4. Build system matrix M from correspondences
5. SVD on M extract P from last column of V
6. Denormalize P
7. RQ-decompose P into K · [R | t]